QCFP.02 package
The QCFP package is a set of C++ programs that perform various tasks related to spectroscopy measurements of molecular excited states. Currently it calculates Fourier transforms of the linear response function and the third order response function of a generic multilevel system and an excitonic model. Essentially all models can be finally represented by a generic multilevel system. So the generic calculation can be ran when transformation is realized by a user-made transformer.
# QCFP requirements on a unix-like system
static development libraries: fftw3 lapack blas
gnu make,
gnu gcc (tested on 5.5.0 version) or clang llvm compilers.
QCFP package has been tested on a range of Linux (Ubuntu, OpenSuse, Mageia), FreeBSD UNIX, clang compilers on Macosx as well as CygWin environment in Windows 10.
# Compilation
Enter into the top folder (there must be a makefile). Edit the text file
make.inc
to point to correct compiler and issue whatever compiler and linker options are necessary on your system. Then run
make
The programs should compile (warnings depend on compiler). To set up
bin/
folder, run
make binaries
To clean up the compilation process, run
make clean
This will restore the package into its original precompiled state.
# Using QCFP
## Running the package
The main executable (with a variable prefix) is in the
bin/
folder:
calculator-main
The calculator is initiated from a command line as follows:
executable inp-file out-file
inp-file
is the text input file, which describes all necessary parameters for the system, the environment and the experiment,
out-file
is the file which will be created by the calculator and where the computed resut will be written.
## Input file
The input file is the text file organized into five parts:
selection-of-calculation
system-type
bath-type
experiment-type
list of parameters
## First part of the input file
Possible values for selection-of-calculation
1st-Absorption-Secular
Calculates the linear response real (absorption spectrum) and imaginary (dispersion) parts as a function of frequency derived from FFT of interaction delay time by the density matrix method secular approximation. Approaches based on simple phenomenological dephasing, secular Redfield, or secular modified Redfield with cumulant lineshape functions are possible.
1st-Absorption-Reduced
Calculates the linear response real (absorption spectrum) and imaginary (dispersion) parts using density matrix method beyond secular approximation. Approaches based on full Redfield, specific cases of Lindblad superoperators and non-markovian Redfield is possible.
1st-Absorption-Wavefunctions
Calculates the linear response real (absorption spectrum) and imaginary (dispersion) parts using wavefunction method. Approaches based on Davydov D2 Ansatz is possible.
3rd-2D-Secular
Calculates the third order optical response function (real and imaginary parts) as a function of two frequencies derived from FFT of two chosen interaction delay times by the same methods as 1st-Absorption-Secular
3rd-2D-Reduced
Calculates the third order optical response function (real and imaginary parts) as a function of two frequencies derived from FFT of two chosen interaction delay times by the same methods as 1st-Absorption-Reduced
3rd-2D-Wavefunctions
Calculates the third order optical response function (real and imaginary parts) as a function of two frequencies derived from FFT of two chosen interaction delay times by the same methods as 1st-Absorption-Wavefunctions
## Second part of the input file
system-type
This is a compound word with the properties separated by dashes (for example System-Excitonic-Paulionic-2band). The word can contain the following items:
Eigensystem
(default) The rest of the system is described in the generic multilevel (eigenstate basis) representation
Exciton
The system is an excitonic system described in molecular (site) representation.
Bosonic
Excitonic system made of anharmonic oscillators (for 2band properties)
Paulionic
(default) Excitonic system made of two-level oscillators (for 2band properties)
2band
Turns on the second manifold of excited states
## Third part of the input file
bath-type
This is a compound word with the properties separated by dashes (for example harmonic-superohmic-bath-UnCorrelated). The word can contain the following items:
Correlated
All fluctuations in the system are taken as correlated and correlation coefficients will have to be provided.
UnCorrelated
All fluctuations in the system are taken as uncorrelated and only autocorrelation coefficients will have to be provided.
## Fourth part of the input file
experiment type
This is a compound word with the properties separated by dashes (for example Experiment-2DES-WTW). The word can contain the following items:
2DES
a must-have word for calculation of third order signals that allows calculation of the 2D spectrum
WTW
calculates rephasing, non rephasing or pump-probe 2D w1 w3 spectrum as a function of t2. these selections are done by choosing specific diagrams.
TWW
calculated 2D w2 w3 spectrum as a function of t1 delay time.
WWT
calculated 2D w2 w3 spectrum as a function of t1 delay time.
Isotropic
Turns the isotropic orientational averaging on
Secular
(only for Reduced calculation – see first part of the input file) Restricts all diagrams to secular approximation
NonSecular
(only for Reduced calculation – see first part of the input file). Allows nonsecular propagation in simulation of optical signals.
Markovian
(only for Reduced and Secular calculation – see first part of the input file). Adds Markovian approximation in simulation of optical signals.
NonMarkovian
(only for Reduced and Secular calculation – see first part of the input file). Allows non Markovian propagation in simulation of optical signals
Lindblad
(only for Reduced calculation – see first part of the input file). Uses Lindblad form of relaxation superoperator in Markovian nonsecular propagation in simulation of optical signals
NoComplexLifetimes
(only for Secular calculation – see first part of the input file). Approximates the finite-lifetime-induced dephasing constants by only their real parts (Lamb-shifts are ignored).
## Fifth part of the input file.
Here all parameters are provided as
keyword:
data

keyword:
data

…

Important to keep track of units that are used. All time units must be the same. All frequency and energy units are the same and identical (I. e. the reduced Planck constant hbar = 1). Default units that are used are reciprocal centimeters for energy and frequency and its inverse, I. e. centimeters are used for time. Default units for distance should be centimeters as well. The other possibilities are combinations
cm-fs-an
these are recoprocal centimeters for energy, femtoseconds for time, angstroms for distance
ev-ps-nm
these are electronvolts for energy, picoseconds for time, nanometers for distance
th-ps-nm
these are terahertz for energy, picoseconds for time, nanometers for distance
defined via keyword:
AllUnits:
combination

## System parameters
EigensysNumberOf01Levels:
number
Total number of levels in 0 and 1 bands in the multilevel case.
EigensysNumberOf012Levels:
number
Total number of levels in 0, 1 and 2 bands in the multilevel case.
EigensysLevelEnergies:
number
number
…
Ordered list of energies for the levels starting from 0 band, then 1 (then 2 if 2band is selected). Bare model without reorganization energies.
EigensysTransitionDipoles:
number_of_entries
number_from number_to number_x number_y number_z
number_from number_to number_x number_y number_z
…
List of relevant electric transition dipoles. First the number of lines-to-read is provideed. Then each line specifies the two levels to be connected by the transition dipole. Levels are numbered in the same order as the level energy list. Indexing starts from 0. Units here are important only when computing CD signal.
EigensysTransitionDipoles:
number_of_entries
number_from number_to number_x number_y number_z
number_from number_to number_x number_y number_z
…
List of relevant electric transition dipoles. First the number of lines-to-read is provideed. Then each line specifies the two levels to be connected by the transition dipole. Levels are numbered in the same order as the level energy list. Indexing starts from 0. Units (el*A) here are important only when computing CD signal.
EigensysMagneticDipoles:
number_of_entries
number_from number_to number_x number_y number_z
number_from number_to number_x number_y number_z
…
List of relevant magnetic transition dipoles. First the number of lines-to-read is provideed. Then each line specifies the two levels to be connected by the dipole. Levels are numbered in the same order as the level energy list. Indexing starts from 0. Units here are …
EigensysQuadrupoles:
number_of_entries
n_from n_to n_xx n_xy n_xz n_yx n_yy n_yz n_zx n_zy n_zz
n_from n_to n_xx n_xy n_xz n_yx n_yy n_yz n_zx n_zy n_zz
…
List of relevant electric transition quadrupoles. First the number of lines-to-read is provideed. Then each line specifies the two levels to be connected by the transition quadrupole. Levels are numbered in the same order as the level energy list. Indexing starts from 0. Units here are el*A*A.
ExcNumberOfSites:
number
Number of sites (molecules) in the excitonic model.
ExcMainHamiltonian:
n11
n21 n22
n31 n32 n33
…
Excitonic main Hamiltonian. Bare electronic model without reorganization energies.
ExcBiparticleAnharmonicites:
n11
n21 n22
n31 n32 n33
…
Biexcitonic binding energies. Often referred as K-couplings, anharmonicities. Bare electronic model without reorganization energies.
ExcElectricDipoles:
number_x number_y number_z
number_x number_y number_z
…
List of electric transition dipoles. The number of rows is the same as the number of sites. Dipoles are numbered in the same order as the Hamiltonian organization. Units (el*A) here are important only when computing CD signal.
ExcPositionVectors:
number_x number_y number_z
number_x number_y number_z
…
List of site coordinates. The number of rows is the same as the number of sites. Entries are numbered in the same order as the Hamiltonian organization. Units here are important only when computing CD signal.
ExcMagneticDipoles:
number_x number_y number_z
number_x number_y number_z
…
List of internal site magnetic transition dipoles. The number of rows is the same as the number of sites. Dipoles are numbered in the same order as the Hamiltonian organization. Units (???) here are important only when computing CD signal.
ExcElectricDipoleAnharmonicities:
number_x number_y number_z
number_x number_y number_z
…
List of transition dipole corrections for bi-excitonic states in bosonic model. The model is that the transition dipole of 1→2 is equal to sqrt(2)*(d_1+d_1_correction). The number of rows is the same as the number of sites. Dipoles are numbered in the same order as the Hamiltonian organization. Units (el*A) here are important only when computing CD signal.
## Experiment parameters
ExperimentNaturalLinewidth:
number
Defines the elementary spectral linewidth (experimental resolution). Needed for proper convergence and smoothing.
ExperimentPolarizations:
px py pz
px py pz
….
The polarizations are ordered as 1-st row = 1-st interaction, etc. For linear response only two polarizations are read. For 3-rd order response, four polarizations are read. The last polarization is that of detector.
ExperimentWavevectors:
kx ky kz
kz ky kz
…
The wavevectors are laser propagation direction unit vectors. In collinear case, these can be zzzz. The input vectors are ordered as 1-st row = 1-st interaction, etc. For linear response only two wavevectors are read. For 3-rd order response, four wavevectors are read. The last wavevector is that of detection field.
ExperimentInteractionFrequencies:
number1
number2
…
The central frequencies of interaction fields. These are used to compute wavevectors.
ExperimentInitialFrequency:
number
Defines the initial frequency in the calculation of linear spectrum.
ExperimentFinalFrequency:
number
Defines the final frequency in the calculation of linear spectrum.
ExperimentNumberOfPoints:
number
Defines the number of points in the calculation of linear spectrum and 3-rd order 2D spectrum for one dimension.
ExperimentDiagramTypes:
n n n n n n n n n n n n n n
14 numbers on the row. n is either 0 or 1 to turn specific type of third order diagrams on or off. Default – rephasing diagrams are on so 2D WTW rephasing can be computed without this entry. The types in the same order are the following:
rep-coherent-gsb
rep-transport-gsb
rep-coherent-ese
rep-transport-ese
rep-coherent-esa
rep-transport-esa
nrp-coherent-gsb
nrp-transport-gsb
nrp-coherent-ese
nrp-transport-ese
nrp-coherent-esa
nrp-transport-esa
2qc-coherent-es1
2qc-coherent-es2
Notice that transport and coherent are distinguished only in the case of secular approach.
ExperimentInitialFrequency1:
number
Defines the initial frequency of omega1 in 2d grid in the calculation of 2D spectrum.
ExperimentFinalFrequency1:
number
Defines the final frequency of omega1 in 2d grid in the calculation of 2D spectrum.
ExperimentInitialFrequency2:
number
Defines the initial frequency of omega2 in 2d grid in the calculation of 2D spectrum.
ExperimentFinalFrequency2:
number
Defines the final frequency of omega2 in 2d grid in the calculation of 2D spectrum.
ExperimentInitialFrequency3:
number
Defines the initial frequency of omega3 in 2d grid in the calculation of 2D spectrum.
ExperimentFinalFrequency3:
number
Defines the final frequency of omega3 in 2d grid in the calculation of 2D spectrum.
ExperimentDelay1:
number
Defines the delay time t1 in the calculation of 2D spectrum.
ExperimentDelay2:
number
Defines the delay time t2 in the calculation of 2D spectrum.
ExperimentDelay2:
number
Defines the delay time t3 in the calculation of 2D spectrum.
## Parmeters relevant for simulations
MethodSpeedUpSmallness:
number
(only for Secular calculation – see first part of the input file). The number parameter is between 0 and 1. This parameter skips diagrams that have probabilities less than the given number. The simulation time can be considerably reduced in certain cases.
MethodPropagatorNumericTimestep:
number
(only for Wavefunction calculation – see first part of the input file). The number is the timestep for integration of the equations of motion.
MethodSizeOfThermalEnsemble:
number
(only for Wavefunction calculation – see first part of the input file). The number is the size of the thermal ensemble. This is necessary for wavefunction calculation because the final result of a system at a finite temperature is essentially the integral over the individual fluctuating trajectories.
MethodSelectPathway:
num1 num2
(only for 1st-Absorption-Secular calculation – see first part of the input file). Only optical transition between num1 and num2 eigenstates is included in the calculation.
## Bath parameters
BathTemperature:
number
Temperature of the bath in Kelvin.
BathNumberOfOscillators:
number
The number of bath spectral densities to read.
BathSpectralDensities:
filename
filename
…
List of bath spectral densities given in separate files. See separate section on the spectral density file.
BathSystemCorrelatedCouplingMagnitudes_I:
kIij
gIij
…
Here I is the number 0<=I<Number of bath spectral densities
ExcBathSystemCouplingMagnitudes:
number_M11 number_M12 … number_M1N
number_M21 number_M22 … number_M2N
…
Coupling constants of sites to different oscillators represented by spectral densities. Here Mij is the matrix of coupling constants – factors in front of reorganization energies. Indices i – spectral density, j- excitonic site.
ExcBathSystemCorrelatedCouplingMagnitudes:

BathSpecificModes:
number_of_modes
number_w1 number_c1 number_c2… number_cN
number_w2 number_c1 number_c2… number_cN
number_w3 number_c1 number_c2… number_cN
...
Coupling term is |n><n|*w*c*q. The reorganization energy of that mode is L=w(c^2)/2, HR parameter is S=(c^2)/2.

***********
## Spectral density file

It is a special file format (text file)
for the spectral density as a function of energy (frequency) - the same units as energy in the input file (e. g. cm-1)
First two lines (starting with “#”) are necessary
then the numbers are
1000 -> the number of points N in the function
0.5 -> the frequency step
0.0
0.32
0.64
and so on are the values of the spectral density at frequencies i*step, where i goes from 0 to N-1

so in principle you can define and use an arbitrary function
what is important is to ensure that the fine details are properly captured (step is not too large)
and the spectral density decays (N is large enough)
## Intermediate files:
Be careful: the calculators generate intermediate files
*.wrk
these files are used whenever you restart calculation.
It is safe to use them if you keep the same spectral density AND temperature.
Delete all *.wrk files if one of these has been changed

**************
Try it and let me know how it goes.